## Slide 1: WiBi: Biased Medium Access Control for WiFi
Cameron Keith, Anna Carroll, Ethan Busbee, Dylan Fansler

## Slide 2: Intro
Presenting WiBi
  a biased Medium Access Control (MAC) protocol for WiFi
Standard WiFi
  Slotted Aloha
    Carrier Sense Multiple Access and Collision Avoidance (CSMA/CA)
  A fair packet access scheme
    Similar to Processor Sharing
Biased scheduling approaches
  Shortest Remaining Processing Time (SRPT)
  Yield better throughput and faster expected completion times than PS
The WiBi MAC approximates SRPT
  Greater throughput and utilization of the wireless medium
WiBi Operation
  Each node chooses a maximum potential back off time
    Proportional to the number of packets that are ready to send

## Slide 3: Our Approaches
SRPT
Current number of frames with random backoff
Dynamic backoff based on congestion

## Slide 4: SRPT
Based on Shortest Remaining Processing Time for Processor Scheduling.
The maximum for the Random Back off is based on the number of Remaining Frames
Under 0.8 load, 80% of node traffic improves by factor of 10
Helps small frame sizes substantially, only slightly penalizes large frame sizes.

## Slide 5: Frame Counter
The Maximum random back off is based on the current Frame number being sent

## Slide 6: Dynamic Backoff
A node sends at a standard rate, periodically checking the network traffic level. If the traffic level appears to hit a certain level, the node checks its own rate and will slow down its transmission rate based on traffic levels.

## Slide 7: Conclusion
It is indeed possible to increase the throughput for 802.11 using a biased MAC protocol.

## Slide 8: Related Work
SRPT: Our work regarding SRPT was based off of a similar problem regarding scheduling requests to a web server. Web server interacts on the application layer, has to worry about things such as collisions and data loss. This caused the advantage of SRPT in wireless networks to diminish. However, due to the point-to-point nature of the MAC sub-layer, data loss due to routing is not something we need to worry about.
Frame Counter: This is a variation of slotted aloha, however instead of a static backoff counter, a random backoff based on the frames left to send is utilized whenever a collision occurs.